## Slide 1: Decoded 1 – Intro & Accessibility Requirements
Audio - US & Canada: 866-430-4132
Audio - International: 404-665-9207
Audio Code: 781-453-5306
Mute your phone (*6 to mute, #6 to unmute).
This webinar is being recorded.

## Slide 2: Decoded 1 – Intro & Accessibility Requirements

## Slide 3: Lori Greene, AHC/CDC, CCPR, FDAI
  Manager, Codes & Resources
  25+ years in the industry
  19 years with Allegion / IRST / rep
  Previous Positions
    Spec Team Leader – New England
    Specwriter
    Customer Service / Tech Support for manufacturer’s rep
    Distributor Experience Prior

## Slide 4: iDigHardware / iHateHardware.com
P4

## Slide 5: Session 1 – Intro & Accessibility
Brief overview of some codes and standards which impact the door and hardware industry.
Who is the AHJ?
Resources for code information.
How codes affect our business.
Code development process and tragic fires that have shaped current codes.
Accessibility Requirements

## Slide 6: Which code / standard applies to your project?

## Slide 7: Door & Hardware Institute COR140 Challenge Exam
COR140 exam will reference:
    2009 IBC
    2009 NFPA 101
    2009 A117.1
    2007 NFPA 80
Download the correct editions of the codes and standards.
Mark them up so you can find the right section quickly and easily.
Allegion code booklet contains references for all editions – available soon!

## Slide 8: Commentary / Handbook

## Slide 9: Some state and local codes differ from the national codes discussed here. Get familiar with your local code requirements!
P9

## Slide 10: How codes affect our business…
The use of many products is code-driven:
    Panic hardware / fire exit hardware
    Fire doors, closers, positive latching
    Delayed egress locks
Codes affect the selection of almost every hardware item:
    Hinges, latches, closers, protection plates, gasketing
    Electrified hardware
    Fire doors

## Slide 11: Authority Having Jurisdiction (AHJ)
Building Inspector
Fire Marshal
Insurance Inspector
Joint Commission (hospitals)
Health Inspector
Electrical Inspector
Others

## Slide 12: Building Codes Forum
Thousands of members, many AHJs
We have our own forum – Door & Hardware Forum

## Slide 13: Code change is often prompted by tragedy
Iroquois Theater Fire (1903)
    603 killed
Triangle Shirtwaist Factory (1911)
    146 killed
Cocoanut Grove (1942)
    492 killed
Station Nightclub (2003)
    100 killed
Many other fires

## Slide 14: Why do we have codes?
Without enforceable codes we would have more tragedies like these.
People who did not comply with the requirements would not be held accountable.
We learn from the past and make code changes to avoid these problems in the future.

## Slide 15: Code Development Process
Prior to 2000, there were 3 model codes in the US – now called the Legacy Codes
    BOCA National Building Code
    UBC Uniform Building Code (aka ICBO)
    SBCCI Standard Building Code
Organizations worked together to create the 2000 International Building Code.
NFPA also publishes a building code – NFPA 5000.

## Slide 16: Code Development Process
Codes and standards are typically revised every 3 years.
Anyone can submit a code change proposal.
Proposals are approved, disapproved, or modified at the code hearings.
The public may comment on the changes.
I participate through the BHMA Codes & Government Affairs Committee

## Slide 17: Accessibility
A117.1 vs. ADA vs. Others
Clear Width
Maneuvering Clearance
Hardware & Thresholds
Closing Speed & Opening Force
Flush Bottom Rail
Vision Lite Location

## Slide 18: Accessibility Standards
A117.1 – Accessible and Usable Buildings and Facilities
ADA – Americans with Disabilities Act Standards for Accessible Design
UFAS – Uniform Federal Accessibility Standards
Fair Housing Act
State Standards
Others
P18

## Slide 20: Clear Opening Width
P20

## Slide 22
Swing clear
hinges can help
increase the clear
opening width.

## Slide 23
5’ equal pairs are
not compliant
At least one leaf must provide 32” clear measured from face of door open at 90 degrees to edge of inactive leaf.

## Slide 24
>24” deep
36” minimum

## Slide 25: Projections Into Clear Width
No projections into the required clear opening width lower than 34” above the floor.
Projections into the required clear opening width between 34” and 80” above the floor shall not exceed 4”.
No Proj.
4”Max.

## Slide 26
May not project more than 4” into the REQUIRED minimum clear width of 32”.
32” clear min.

## Slide 27
4’ wide door
32” clear
minimum
May not project more than 4” into the REQUIRED minimum clear width of 32”.

## Slide 31: Maneuvering Clearance

## Slide 38: Thresholds
P38

## Slide 39
Threshold
Ramp

## Slide 41: Door Hardware
P41

## Slide 43: Lever Handles
In California, the lever has to return to within ½” of the face of the door.

## Slide 44: Thumbturns
Size is not specified by the standards.
No grasping, tight pinching, or twisting the wrist.
Accessibility standards are not specific.
GOOD
???

## Slide 45: Pulls
Projection of pull is not specified by ADA or A117.1.
Pull should be open so hand can slide through.
Accessibility standards are not specific.
GOOD
???

## Slide 46
Hardware must be mounted between 34” and 48” AFF.

## Slide 47: Sliding Doors
When fully open, operating hardware exposed and usable from both sides
Surface-mounted pulls are required, and the door does not retract fully into the pocket.
Affects clear opening width.
NOT Accessible

## Slide 49: Closing Speed
P49

## Slide 51: Opening Force
P51

## Slide 54: Adjustments of a Door Closer
Closing Speed
Closing Force

## Slide 55: Door Surface
P55

## Slide 60: Vision Lites
P60

## Slide 65: Power-Operated Doors
Full-Power Operated automatic doors – comply with ANSI/BHMA A156.10

## Slide 66: Power-Operated Doors
Power-Assist and Low Energy – comply with ANSI/BHMA A156.19

## Slide 67: Requirements of A156.19 for low energy operators
Initiated by a “knowing act”
    Wall- or jamb-mounted push button
    Touchless switches
    Opening the door
    Access control - keypad, card reader, keyswitch
  Low energy operators not initiated by a knowing act must follow the requirements of A156.10.

## Slide 68: Requirements of A156.19
Knowing Act Switches
    1’ to 5’ from door preferred, 12’ maximum
    Accessible from swing side with door open
    User not in path of moving door
    User in full sight of door when activating switch
    34” to 48” a.f.f.

## Slide 69: Requirements of A156.19
Open/close slowly
Stay open for 5 seconds
Closing Force – 15 pounds maximum
Opening Force
    15 pounds to release latch
    30 pounds to set door in motion
    15 pounds to fully open
Signage

## Slide 70: Tactile Warning - UFAS
4.29.3* TACTILE WARNINGS ON DOORS TO HAZARDOUS AREAS. Doors that lead to areas that might prove dangerous to a blind person (for example, doors to loading platforms, boiler rooms, stages, and the like) shall be made identifiable to the touch by a textured surface on the door handle, knob, pull or other operating hardware. This textured surface may be made by knurling or roughing or by a material applied to the contact surface. Such textured surfaces shall not be provided for emergency exit doors or any doors other than those to hazardous areas.
This requirement does not appear in the ADA or A117.1.

## Slide 71: 2010 ADAAG – Automatic Doors (not in A117.1)
404.3.1 Clear Width. Doorways shall provide a clear opening of 32 inches (815 mm) minimum in power-on and power-off mode. The minimum clear width for automatic door systems in a doorway shall be based on the clear opening provided by all leaves in the open position.
404.3.2 Maneuvering Clearance. Clearances at power-assisted doors and gates shall comply with 404.2.4. Clearances at automatic doors and gates without standby power and serving an accessible means of egress shall comply with 404.2.4.
EXCEPTION: Where automatic doors and gates remain open in the power-off condition, compliance with 404.2.4 shall not be required.

## Slide 73: 2010 ADAAG - Operation
404.2.7 Door and Gate Hardware. Handles, pulls, latches, locks, and other operable parts on doors and gates shall comply with 309.4. Operable parts of such hardware shall be 34 inches (865 mm) minimum and 48 inches (1220 mm) maximum above the finish floor or ground. Where sliding doors are in the fully open position, operating hardware shall be exposed and usable from both sides.

## Slide 74: 2010 ADAAG - Operation
309.4 Operation. Operable parts shall be operable with one hand and shall not require tight grasping, pinching, or twisting of the wrist. The force required to activate operable parts shall be 5 pounds (22.2 N) maximum.
EXCEPTION: Gas pump nozzles shall not be required to provide operable parts that have an activating force of 5 pounds (22.2 N) maximum.

## Slide 76: Session 1 – Intro & Accessibility
Brief overview of some codes and standards which impact the door and hardware industry.
Who is the AHJ?
Resources for code information.
How codes affect our business.
Code development process and tragic fires that have shaped current codes.
Accessibility Requirements

## Slide 77: Session 1 – Intro & Accessibility
A117.1 vs. ADA vs. UFAS
Clear Width
Maneuvering Clearance
Hardware & Thresholds
Closing Speed & Opening Force
Flush Bottom Rail
Vision Lite Location

## Slide 78: There are articles about all of these topics on iDigHardware.com.

## Slide 79
P79