## Slide 1: Decoded 3 – Egress and Life Safety
Audio: 866-430-4132, Code: 781-453-5306
Mute your phone (*6 to mute, #6 to unmute)
This webinar is being recorded.

## Slide 2: Decoded 3 – Egress and Life Safety
If you will be taking the COR140 exam, please sign up individually via DHI.org.
40 multiple-choice questions
90 minutes
open book
$450 members, $550 non-members
Audio Dial-In - US & Canada: 866-430-4132
Audio Dial-In - International: 404-665-9207
Audio Code: 781-453-5306
Mute your phone (*6 to mute, #6 to unmute).
This webinar is being recorded.

## Slide 6: Session 3 – Life Safety
IBC – NFPA 101 – IFC
Occupancy Types – Use Groups
Occupied vs. Unoccupied
Opening Protectives
Means of Egress
  travel distance, common path of travel, dead end corridors
  clear width, projections, and door swing
  opening force and auto operators
  unlatching, bolts, hardware operation and height
  panic hardware

## Slide 7: Building Code vs. Life Safety Code or Fire Code
A building code is typically used only during design/construction. After completion, the applicable fire code is enforced.

## Slide 8: Question
What does “Approved” mean when it is used in the IBC or NFPA 101?
Type in the chat box.

## Slide 9: Approved

## Slide 10: Authority Having Jurisdiction

## Slide 11
Occupancy Classifications
(NFPA 101 – Chapter 6)
Assembly
Educational
Day Care
Health Care
Ambulatory Health Care
Detention and Correctional
Residential
Residential Board and Care
Business
Mercantile
Industrial
Storage
Use Groups
(IBC – Chapter 3)
Assembly
Business
Educational
Factory and Industrial
High Hazard
Institutional
Mercantile
Residential
Storage
Utility & Maintenance
Most are divided into sub-groups

## Slide 12: Occupancy Classifications and Use Groups Some are a little tricky…
A college classroom building is a Business occupancy, but if a college classroom holds 50 or more, it is an Assembly occupancy.
NFPA 101’s Ambulatory Health Care occupancy is usually considered Group B (Business) for the IBC.
Child day care centers are considered Day Care occupancies per NFPA 101, but may be I (Institutional) or E (Educational) use groups per the IBC.
A training room within an office building is not considered an Assembly use group by the IBC unless it has an occupant load of 50 or more, or is over 750 sq. ft. in area.
NFPA 101’s Health Care, Board & Care, Detention & Correctional are all I (Institutional) use groups per the IBC.

## Slide 13: Multiple Occupancies (NFPA 101)
6.1.14.2.1 Multiple Occupancy. A building or structure in which two or more classes of occupancy exist.
  6.1.14.2.2 Mixed Occupancy. A multiple occupancy where the occupancies are intermingled. (follow most stringent requirements throughout)
  6.1.14.2.3 Separated Occupancy. A multiple occupancy where the occupancies are separated by fire resistance–rated assemblies. (follow separate requirements for each area)

## Slide 14: Hazard of Contents (NFPA 101)
6.2.2.2* Low Hazard Contents. Low hazard contents shall be classified as those of such low combustibility that no self propagating fire therein can occur.
6.2.2.3* Ordinary Hazard Contents. Ordinary hazard contents shall be classified as those that are likely to burn with moderate rapidity or to give off a considerable volume of smoke. (most buildings are ordinary hazard)
6.2.2.4* High Hazard Contents. High hazard contents shall be classified as those that are likely to burn with extreme rapidity or from which explosions are likely.

## Slide 15: Question
According to NFPA 101, when is a building considered “occupied”?
Type in the chat box.

## Slide 16: Occupied vs. Unoccupied (NFPA 101)
NFPA 101 and IFC – some requirements differ for times when the building is open or occupied by more than 10 people.
IBC – very little difference in requirements for occupied vs. unoccupied

## Slide 17
Chapter 7 Means of Egress
Chapter 8 Features of Fire Protection
Chapters 12-42 Occupancy Chapters
Chapter 7 Fire and Smoke Protection Features
Chapter 10 Means of Egress

## Slide 18: Opening Protectives (NFPA 101)

## Slide 19: Opening Protectives – (IBC)

## Slide 20: Means of Egress
A continuous and unobstructed way of travel from any point in a building or structure to a public way
Not every door is an egress door.
Not every egress door has an exit sign.

## Slide 23: Means of Egress
Exit Access – leads from occupied portion to an exit
Exit – separated by fire-resistance-rated construction and opening protectives to provide a protected path of egress travel
Exit Discharge – between termination of an exit and a public way
Exit
Exit Discharge
Exit
Access

## Slide 24: Exit Passageway

## Slide 25: Exit Passageway

## Slide 26: What is this?
P26

## Slide 27: This is not an exit passageway. It is an exit access.

## Slide 28: Means of Egress
Exit Access – leads from occupied portion to an exit
Exit – separated by fire-resistance-rated construction and opening protectives to provide a protected path of egress travel
Exit Discharge – between termination of an exit and a public way
Exit
Exit Discharge
Exit
Access

## Slide 29: Exit / Exit Enclosure

## Slide 30: Horizontal Exit
P30

## Slide 31: Horizontal Exit

## Slide 32: Horizontal Exit

## Slide 33: Area of Refuge
NFPA 101
IBC

## Slide 34: Area of Refuge

## Slide 35: Travel Distance
Travel distance may end at the beginning of an exit, at an exit discharge, or at a horizontal exit.

## Slide 36: Travel Distance

## Slide 37: Example from New Educational Chapter

## Slide 38: Question
What is the common path of travel?
Type in the chat box.

## Slide 39: Common Path of Travel

## Slide 40: Common Path of Travel

## Slide 41: Common Path of Travel Example from Existing Educational Chapter

## Slide 42: Dead End Corridors
Ex:

## Slide 43: Dead End Corridors
Ex:

## Slide 44: Courtyards, Terraces, and Roofs

## Slide 45: Courtyards, Terraces, and Roofs

## Slide 46: Courtyards, Terraces, and Roofs

## Slide 47
Courtyards, Terraces, and Roofs

## Slide 48: Readily Distinguishable
Means of egress doors must be visible.
  No mirrors
  No drapes
  No decorations
No invisible doors!

## Slide 53: This was approved by the AHJ.

## Slide 54: Also approved by the AHJ.

## Slide 55: Luminous Egress Path Markings

## Slide 56: Luminous Egress Path Markings
Not currently required by NFPA 101 occupancy chapters
Required by IBC in high-rise buildings in Group A – Assembly, B – Business, E – Educational, I – Institutional, M – Mercantile, and R-1 – Residential
Typically required on exit discharge doors – not on doors leading to the exit.
1” stripe around frame
Marking on or behind hardware
“Exit” in bottom 18” of door
Additional marking on stairs, walls, etc.

## Slide 57: Size of Doors
32” clear width minimum
  Measured with door open to 90 degrees
  Between the face of the door and the stop
  At least one leaf of a pair must comply
48” wide nominal max. (IBC/IFC only – not NFPA 101)
80” high nominal min.
78” to the closer arm

## Slide 58: Question
The clear opening width of a newly-installed door measures 31”. What is a possible solution?
Type in the chat box.

## Slide 59: Swing Clear Hinges
May be used to gain more clearance on existing openings.

## Slide 62: Projections Into Clear Width (IBC)
No projections into the required clear opening width lower than 34” above the floor.
Projections into the required clear opening width between 34” and 80” above the floor shall not exceed 4”.
No Proj.
4” Max.

## Slide 63: Projections Into Clear Width (NFPA 101)
NFPA 101 limits the 4” projections to 34”-48” above the floor, hinge side only, only to address panic hardware.
No Proj.
4” Max.

## Slide 64
May not project more than 4” into the REQUIRED minimum clear width of 32”.
32” clear min.

## Slide 65
4’ wide door
32” clear
minimum
May not project more than 4” into the REQUIRED minimum clear width of 32”.

## Slide 66: Question
When is a door required to swing in the direction of egress?
Type in the chat box.

## Slide 67: Door Swing
Egress doors shall be side-hinged swinging
  Exceptions – consult codes
Swing in the direction of egress:
  When serving an occupant load of 50 or more
  Group H occupancy
  When swinging into an exit enclosure (NFPA 101)

## Slide 68: Encroachment
Must encroach no more than ½ of the required width at any point in door swing
7” maximum encroachment on required minimum width when fully open (be careful of cush closers and o.h. stops)

## Slide 69: Encroachment
Must encroach no more than ½ of the required width at any point in door swing
7” maximum encroachment on required minimum width when fully open (be careful of cush closers and o.h. stops)

## Slide 70: Door Opening Force
Interior swinging egress doors (non-fire-rated) – 5 lbs
Other swinging doors + sliding and folding…
P70

## Slide 71: Door Opening Force
Interior swinging egress doors (non-fire-rated) – 5 lbs
Other swinging doors + sliding and folding
  15 pounds to release latch
  30 pounds to set the door in motion
  15 pounds to swing door to fully-open position
P66

## Slide 72: Power-Operated Doors
P67

## Slide 73: Power-Operated Doors
In the event of a power failure:
  15 pounds to release latch
  50 pounds to set door in motion
  30 pounds to open to fully-open position
Full-Power Operated - A156.10
Power-Assist and Low Energy - A156.19

## Slide 74: Question
What are some of the rules for operating hardware on an egress door?
Type in the chat box.

## Slide 75: Door Operations
Readily openable
No key or special knowledge or effort

## Slide 79
Easy to grasp
Operable with one hand
No tight grasping
No tight pinching
No twisting of the wrist
Hardware
YES!
NO!

## Slide 80: Hardware Height
Operating Devices
  34” minimum AFF
  48” maximum AFF
  Locks used only for security purposes – any height

## Slide 81: Locks & Latches
Permitted to prevent operation of doors where any of the following exists:
  Places of detention or restraint
  Use Group A with an occupant load of 300 or less, Groups B, F, M, and S, and in churches
      Main exterior door
      Key-operated locking from egress side
      Locking device readily distinguishable as locked
      Signage on or adjacent to door
      Revocable by the building official for cause

## Slide 82: Locks & Latches (continued)
Permitted to prevent operation of doors where any of the following exists:
  Individual dwelling or sleeping units of Group R occupancies with an occupant load of 10 or less, one additional… (may vary by local code)
    Nightlatch
    Deadbolt
    Security chain
    No key or tool needed on egress side

## Slide 83: Bolt Locks (IBC)
Manual flush bolts or surface bolts not permitted
Exceptions:
  Doors not required for egress in dwelling units.
  Storage or equipment rooms.
  Group B, F, or S occupancy with an occupant load of less than 50.
  Group B, F, or S occupancy where inactive leaf is not needed to meet egress width requirements and building is fully sprinklered.
  Pairs at hospital patient rooms may have constant latching bolts.
  No dummy hardware on inactive leaf.

## Slide 84: Unlatching
Unlatching any leaf shall not require more than 1 operation
Exception:
  Places of detention or restraint
  Storage or equipment rooms
  Automatic flush bolts
  Individual dwelling units and guestrooms of Group R occupancies

## Slide 88: Panic and Fire Exit Hardware
touchpad style
crossbar style

## Slide 89: Question
According to NFPA 101-2009, where is panic hardware required?
Type in the chat box.

## Slide 90: Panic and Fire Exit Hardware
IBC 2006, 2009, 2012
  Educational and Assembly Occupancies with an occupant load of 50 or more
  All High Hazard Occupancies
IBC 2000, 2003
  Educational and Assembly Occupancies with an occupant load of 100 or more
  Some High Hazard Occupancies
NFPA 101 (all)
  Educational, Assembly, and Day Care Occupancies with an occupant load of 100 or more
  Some High Hazard Occupancies

## Slide 91: Panic and Fire Exit Hardware
Requirement for panic hardware applies to means of egress doors in these occupancy types which latch or lock.

## Slide 92: Panic and Fire Exit Hardware
Where panic hardware is required, actuating portion of device (touch-pad or cross-bar) must be at least half the width of the door.

## Slide 95: Is this acceptable? Type in the chat box.

## Slide 96: Panic and Fire Exit Hardware
15 pounds of force maximum to actuate
One motion to exit - no other locking/latching hardware

## Slide 100: Panic and Fire Exit Hardware
P100

## Slide 101: Panic and Fire Exit Hardware
Panic hardware used on balanced doors must be touchpad style (not crossbar) and touchpad must not extend more than half the width of the door.

## Slide 102: Panic and Fire Exit Hardware
Panic hardware used on balanced doors must be touchpad style (not crossbar) and touchpad must not extend more than half the width of the door.

## Slide 103: NFPA 70 National Electric Code
Rooms housing large equipment - 600 Volts, nominal or less, 1200 amperes or more (2014 NEC: 800 amps)
Rooms housing conductors and equipment used on circuits of over 600 Volts, nominal.
Transformer Vaults (2014: Battery Rooms)
Where the entrance has a personnel door(s), the door(s) shall open in the direction of egress and be equipped with panic bars, pressure plates, or other devices that are normally latched but open under simple pressure. (2014: “listed panic hardware”)

## Slide 104: Glass and Glazing
Glass in fire doors was once exempt from impact-resistant requirements.
Glass in fire doors is no longer exempt per the IBC.
Traditional wired glass is extremely hazardous.
There is A LOT more information about glass on iDigHardware (click the Glass tab)

## Slide 105: Session 3 – Life Safety
IBC – NFPA 101 – IFC
Occupancy Types – Use Groups
Occupied vs. Unoccupied
Opening Protectives
Means of Egress
  travel distance, common path of travel, dead end corridors
  clear width, projections, and door swing
  opening force and auto operators
  unlatching, bolts, hardware operation and height
  panic hardware

## Slide 106: Homework
Find at least one non-compliant egress door.
Photograph the issue and find the applicable paragraph in the 2009 IBC and 2009 NFPA 101 (ie. the paragraph that requires one motion to unlatch, or panic hardware, etc.).
Email photos and documentation to lori.greene@allegion.com.

## Slide 107
P102